## Slide 1: A 4×4 phased-array research platform built from ESP32-C5 radios
5.2 GHz · two 8-element tiles · PARLIO aggregation into one ESP32-S31 per tile · 1 GbE per tile
Student project proposal — technical concept
October 2026
Builds on the open ESPARGOS and ESP-SDR projects. Photo: our existing 4×4 patch board (5.2 GHz, FR4).
Notes: A staged student project: a 16-element 5.2 GHz digital array from ESP32-C5 radios, built as two 8-element tiles. Each tile funnels eight 2-bit PARLIO lanes into one ESP32-S31 and one Gigabit port. The hard parts are synchronization, calibration and getting IQ out of the C5.

## Slide 2: What are we trying to build?
λ = c / 5.2 GHz = 57.7 mm; d = λ/2 = 28.8 mm. Status = shown on ESP32-class hardware (ESPARGOS, 2.4 GHz) — none of it is shown on the C5 at 5 GHz yet.
2
A 16-element digital array at 5.2 GHz in which every element is a complete ESP32-C5 transceiver. The aim is a research platform for receiving, sensing and communication, with coherent transmission as a later research question.
One element (×16)
Patch + SPDT
5.2 GHz, ANT / CAL
ESP32-C5
RF transceiver, raw IQ
2-bit PARLIO
80 Mbit/s lane
ESP32-S31
8 lanes → 1 GbE
48 MHz reference
5.2 GHz calibration tone
trigger / timestamp
Shared by all 16 elements — this is what turns 16 radios into one array.
28.8 mm
86.5 mm between outer element centres
4 × 4 elements
λ/2 pitch at 5.2 GHz
no grating lobes for
±90° scan
Receive
digital beamforming, AoA / direction finding (shown by ESPARGOS at 2.4 GHz)
Sense
Wi-Fi sensing, passive and bistatic radar, Doppler
Sound
channel sounding, MIMO measurements, localization
Transmit coherently
TX beamforming, if raw TX can be reproduced
Confirmed
Engineering inference
Speculative
Notes: Every element is a complete C5 transceiver with a calibration switch in front. The status markers are strict: 'confirmed' means shown on ESP32 hardware (ESPARGOS, 2.4 GHz), not on the C5 at 5 GHz.

## Slide 3: What already exists, and what is new here
Sources: ESPARGOS One datasheet (June 2026), espargos.net, pyespargos, arXiv 2502.09405; ESP-SDR page and repository (HEAD 2026-10-08).
3
ESPARGOS (Univ. of Stuttgart)
ESPARGOS One: 8 ESP32-C61 sensors + a controller ESP32; 4 × 2 dual-polarized patches, 2.4 GHz
shared 40 MHz clock + 2.4 GHz reference through a splitter and an RF switch at every sensor
PLL phase changes after every reset and channel change, so calibration is repeated per configuration
raw IQ (closed firmware): wired trigger, packet timestamps ≤ 37.5 ns apart, CW tone from the controller’s PLL
up to 4 boards (32 elements) combined; clock + reference share one SMA cable in a star
ESP-SDR
raw IQ from an undocumented modem sample-dump engine; 10 chips; open source since Sept 2026
ESP32-C5 receives at 5 GHz: a 5.5 GHz test tone, and a second C5 on channels 36/48 (5.17–5.25 GHz)
C5: snapshots of ≤ 16,380 samples at up to 80 MS/s, 10-bit I/Q, sent over USB or UART
software trigger only; no timestamps, no multi-device synchronization
receive-only; ESP-SDR's CPU spectrum mode on the C5 returns power, not complex bins
What this project adds
the ESPARGOS synchronization principle at 5.2 GHz with a 48 MHz reference
one external 48 MHz clock driving 16 chip-down ESP32-C5s; C5 LO-phase behaviour
hardware trigger and capture alignment for C5 snapshots
IQ export over 2-bit PARLIO into one ESP32-S31 per tile, then 1 GbE
in-band 5.2 GHz calibration network; two 8-element tiles with a master timing board
Confirmed
Engineering inference
Open — needs bench test
Speculative
Notes: ESPARGOS proves the synchronization recipe; ESP-SDR proves raw IQ from the C5 at 5 GHz. Neither gives a synchronized, triggered, fast multi-C5 capture — that is our new work.

## Slide 4: Why ESP32-C5?
Sources: Espressif datasheets (C5 v1.5, S31 v0.5 pre-release, others current); ESP-SDR README chip-support table. Checked 12 Oct 2026.
4
Chip | Wi-Fi | 5 GHz | Main crystal | Relevance here
ESP32-C5 | Wi-Fi 6, 2412–2484 + 5180–5885 MHz | yes | 48 MHz | only 5 GHz part; separate ANT_5G pin; ESP-SDR snapshot IQ
ESP32 | Wi-Fi 4, 2.4 GHz | no | 40 MHz | 2.4 GHz only
ESP32-S2 / S3 | Wi-Fi 4, 2.4 GHz | no | 40 MHz | 2.4 GHz only
ESP32-C2 / C3 | Wi-Fi 4, 2.4 GHz | no | 26 or 40 / 40 MHz | 2.4 GHz only
ESP32-C6 / C61 | Wi-Fi 6, 2.4 GHz | no | 40 MHz | C61 is the sensor in ESPARGOS One
ESP32-H2 | none (BLE, 802.15.4) | no | 32 MHz | no Wi-Fi; ESP-SDR still receives
ESP32-S31 | Wi-Fi 6, 2.4 GHz | no | 40 MHz | continuous IQ streaming in ESP-SDR (experimental), 2.4 GHz only
Only the ESP32-C5 reaches 5.2 GHz natively. ESP-SDR receives on all ten parts, but every other chip would need an external mixer and LO per element to reach 5.2 GHz — which defeats the point of a low-cost array. The price: the C5 has no continuous IQ path today.
Notes: Only the C5 reaches 5.2 GHz. The S31 is 2.4 GHz only, which is why it serves as the tile's digital and network aggregator rather than as an RF element.

## Slide 5: The antenna board we already have
Observations from photos; pitch and patch size to be confirmed against the layout files. Patch estimate: transmission-line model, εr = 4.5, h = 1.52 mm.
5
radiating side: 16 probe-fed patches + 4 test patches
back: one SMA per element
What we can read off it
4 × 4 rectangular patches, linear polarization
silkscreen: f₀ = 5.2 GHz, FR4 εr = 4.5, h = 60 mil
pitch ≈ 30 mm from the ruler, consistent with λ/2 = 28.8 mm
expected patch ≈ 13 × 17 mm — matches the proportions
What it means
Rev 1 can use this board as the aperture and cable each element to its tile — no seam crosses the radiating surface.
Or the tiles carry their own patches (next section) — then substrate thickness and the seam need care.
Either way, measure S11 and neighbour coupling per element first.
Notes: Our existing 4×4 board is a ready-made aperture. Rev 1 can cable it to the tiles, or the tiles can carry their own patches — the tile PCB slide explains the trade-off.

## Slide 6: The hard part is synchronization
Error model follows the ESPARGOS approach (shared clock + in-band phase reference + digital correction); C5-specific behaviour must be measured.
6
Sixteen independent radios disagree in frequency, phase, timing and gain. A shared clock fixes only the first of these; the rest have to be measured and removed.
Error term | Where it comes from | Shared 48 MHz clock | 5.2 GHz cal. tone | Common trigger
Carrier frequency offset, drift | independent crystals (tens of ppm) | removes | — | —
LO phase offset | each PLL locks with an arbitrary phase | — | removes | —
Sampling-time offset | independent sample clocks and start times | partly | removes (swept tone) | partly
Capture start misalignment | firmware / interrupt latency | — | partly | removes
Fixed path mismatch | cables, PCB traces, switches, filters | — | after the switch | —
Gain mismatch | AGC state, LNA spread | — | if gain is fixed | —
Uncorrelated phase noise | additive jitter of buffers, PLL noise | partly | — | —
Consequence: calibration is not a one-off factory step. The LO phase changes every time a PLL relocks, so the array must be able to re-measure itself on demand — that is why the calibration network is part of the hardware.
Notes: The shared clock fixes frequency only. LO phase, timing and fixed path errors need the in-band reference; ESPARGOS measured that the PLL phase re-rolls after each reset or channel change.

## Slide 7: Four synchronization domains — and what Ethernet is not for
Team architecture; ESPARGOS uses the same split (shared clock, wired trigger, switched RF reference). Ethernet / PTP is for coordination only.
7
Domain | Signal and path | Guarantees | Does not guarantee
RF reference | 48 MHz TCXO → fan-out → 16 × XTAL_P | one frequency for all LOs | LO phase after each lock
Data transport | 40 MHz PCLK → fan-out → 16 C5 + 2 S31 | lane-to-lane cycle alignment | which sample a lane starts with
Capture trigger | master GO → S31 → PCLK enable (+ READY) | common start within a tile | tile-to-tile start (two S31s)
RF calibration | 5.2 GHz tone → 1:2 → 1:8 → SPDT | measures φₖ, τₖ and path mismatch | anything before the switch
Ethernet / PTP | S31 EMAC, 1588 timestamps | logging, tile coordination | sample or phase alignment
Wideband correction per element is a phase plus a delay: Cₖ(f) = exp[−j(φₖ + 2πfτₖ)], applied per FFT bin before the channels are combined.
Notes: Four separate domains: 48 MHz RF reference, 40 MHz data clock, capture trigger, 5.2 GHz calibration. Ethernet and PTP are for logs and coordination, never for sample alignment. Wideband correction is a phase plus a delay per element, applied per FFT bin.

## Slide 8: Sharing one 48 MHz reference
ESP32-C5 HW design guidelines (48 MHz only, ±10 ppm, >500 mV, 24 nH series L); ESP32-S2 HDG oscillator note; TI SWRA029 (20·log N); buffer and TCXO datasheets.
8
48 MHz TCXO
±0.5 ppm, clipped sine
e.g. TG2016SMN
1:2 fan-out
master board
e.g. LMK1C1104
tile B
one cable per tile
tile A (4 of 8 shown)
1:8 buffer
LVCMOS
ESP32-C5 XTAL_P
ESP32-C5 XTAL_P
ESP32-C5 XTAL_P
ESP32-C5 XTAL_P
coupling network
(level per HW guide)
Frequency
All 16 LOs derive from one oscillator, so carrier offsets between elements vanish. The absolute ppm error is common to all and harmless.
Static skew
Buffer skew becomes a fixed LO phase: 50 ps ≈ 94° at 5.2 GHz. Calibration removes it — but skew drifting with temperature shows up as phase drift.
Jitter
In-band reference noise rises by 20·log(5200/48) = 40.7 dB. Jitter common to all elements cancels in relative phase; buffer additive jitter (20–160 fs max ≈ 0.04–0.3°) does not.
Injection
The C5 design guidelines cover only a 48 MHz ±10 ppm crystal, with no external-oscillator requirements (the datasheet calls XTAL_P/N a crystal or oscillator input). Precedents: the ESP32-S2 guide (oscillator into XTAL_P via ~50 pF), ESPARGOS (40 MHz shared), Espressif’s esp-crab (two C5s, “co-crystal”). C5 modules carry their own crystal.
Numbers at 5.2 GHz
N = 5200 / 48 | ≈ 108 (+40.7 dB)
1 ps rms jitter | 1.87° rms
50 ps static skew | 94° (calibrated)
108 × 48 MHz | 5184 MHz — in band
Notes: Espressif documents only a 48 MHz ±10 ppm crystal for the C5; driving XTAL_P from a buffer is our first clock bench test. Static skew becomes static phase and is calibrated out; the 108th harmonic of 48 MHz falls at 5184 MHz.

## Slide 9: A 5.2 GHz calibration network
Adapted from ESPARGOS. MAX2871: VCO 3–6 GHz, −1 to +8 dBm, mutable outputs. SKY13351: 0.35 dB loss, 24 dB isolation at 2.45 GHz (datasheet); less expected at 5 GHz.
9
5.2 GHz source
PLL synthesizer, or a
17th C5 (cf. ESPARGOS)
1:2 splitter
master board
tile B
tile A (4 of 8 shown)
1:8
Wilkinson
SPDT
C5
SPDT
C5
SPDT
C5
SPDT
C5
Each SPDT: upper input from the antenna, lower input from the calibration splitter.
Indicative level budget
Stage | Loss
1:2 + 1:8 split (ideal 3 + 9 dB) | ≈ 14–15 dB
cables + ≈ 18 cm of tile lines | ≈ 5–7 dB
SPDT insertion loss | ≈ 1 dB
source 0 dBm → at each C5 | ≈ −20 to −23 dBm
Well below the C5's +5 dBm maximum input, but enough to clip the 10-bit samples at high gain: attenuate and use one low, fixed gain index. SKY13351-class switches specify ≈ 24 dB isolation (at 2.45 GHz; likely less at 5 GHz), so mute the synthesizer during antenna captures.
Global source or one per tile?
 | Global | Per tile
Inter-tile phase reference | yes, common | none — needs OTA step
RF routing | 2 cables | local only
Cost / parts | 1 source | 2 sources
Tiles testable alone | with a jumper | yes
Proposal: one MAX2871-class source on the master board, a 1:2 split to the tiles, a 1:8 Wilkinson tree and eight SPDTs per tile. Each tile also gets a local test input so it can be calibrated alone during bring-up.
architecture choice, adapted from ESPARGOS
Notes: One MAX2871-class source, split 1:2 to the tiles and 1:8 on each tile, into an SPDT in front of every C5. Fixed attenuation and a fixed low gain index keep the 10-bit samples from clipping.

## Slide 10: Calibration is a measurement loop
Procedure follows ESPARGOS One IQ mode (pyespargos iq_sync / iq_pool): packet-timestamp coarse sync, swept CW tone for (τ, φ), valid for one capture epoch.
10
1
Lock and fix gain
tune all C5s, disable AGC, set the same manual gain
2
Measure the reference
all SPDTs to CAL; step the tone across the band, one snapshot per step
3
Estimate offsets
per element: gain gₖ, phase φₖ; delay τₖ from the phase slope across steps
4
Measure the scene
all SPDTs to ANT; synchronized snapshot(s)
5
Correct
multiply by (gₖ·e^(jφₖ))⁻¹ and remove τₖ before any array processing
repeat after every reset, retune or sample-rate change — ESPARGOS treats a calibration as valid for one capture epoch
Per-element model during a snapshot
yₖ[n] = gₖ · ejφₖ · x(nTₛ − τₖ) + wₖ[n]
In CAL mode x is the common reference, so gₖ, φₖ, τₖ follow from comparing each yₖ with element 1. A single CW tone cannot separate φₖ from τₖ; ESPARGOS sweeps the tone across the band and fits both, after coarse alignment on a shared reference packet.
What the tone cannot see
Everything before the switch: patch, probe via and a 1 mm line, the same for all eight (or the cable, with a separate aperture). Calibrate once over the air; tile B adds a fixed 180°.
Mutual coupling between elements: measure embedded element patterns once the first tile works.
Errors that change faster than the calibration interval.
Notes: Lock, fix gain, measure the reference, estimate gain, phase and delay per element, then measure the scene and correct. ESPARGOS treats a calibration as valid for one capture epoch.

## Slide 11: Sixteen receivers create a data problem
Line rates from datasheets; ESP-SDR uses UART / USB on the C5 today. PARLIO figures are width × 40 MHz. Raw IQ as 8-bit I + 8-bit Q.
11
Chart: Mbit/s (log scale)
| C5 UART (ESP-SDR default) | C5 USB-Serial-JTAG (ESP-SDR) | C5 PARLIO, 2 bit × 40 MHz | C5 PARLIO, 8 bit × 40 MHz | S31 PARLIO, 16 bit × 40 MHz | Gigabit Ethernet | 1 element, 80 MS/s | 16 elements, 20 MS/s | 16 elements, 80 MS/s
Mbit/s | 2 | 12 | 80 | 320 | 640 | 1000 | 1280 | 5120 | 20480
what the array produces
what common links carry
16 × 80 MS/s × 16 bit
= 20.48 Gbit/s
The C5 samples at up to 80 MS/s internally, but ESP-SDR moves captures out over USB (12 Mbit/s) or UART.
A 2-bit PARLIO lane at 40 MHz gives each C5 80 Mbit/s: enough for ~4 MS/s continuous, or for draining full-rate snapshots in a few milliseconds.
Eight lanes fill one 16-bit S31 bus (640 Mbit/s) and one Gigabit port per tile — a rate ESP-SDR already pushes through an S31 (≈ 687 Mbit/s on the wire). Continuous raw 80 MS/s from 16 elements stays out of scope.
Notes: The internal rate (80 MS/s) is not the export rate. ESP-SDR exports over USB or UART today. A 2-bit PARLIO lane gives 80 Mbit/s per C5, eight lanes 640 Mbit/s per tile — the same rate ESP-SDR already pushes through an S31 to Gigabit Ethernet.

## Slide 12: What ESP-SDR gives us today: snapshots, not streams
ESP-SDR C5 limits from chip.h (IQ_WORDS = 16,380), README and PR #9 (retune time). Transfer times are upper bounds from line rates — no measured C5 snapshot rate is published.
12
One element, snapshot mode
capture
transfer to host / tile
re-arm
capture
transfer to host / tile
re-arm
capture
…
time
The largest C5 snapshot is 16,380 complex samples: 204.75 µs at 80 MS/s, 32,760 bytes as 8-bit I/Q. Moving it out takes 100–1000× longer than capturing it, so the duty cycle is set by the output port, not by the ADC.
Best case for one 16,380-sample IQ8 snapshot
Output port (per element) | Transfer time | Snapshots / s | Duty cycle
UART, 2 Mbaud (ESP-SDR today) | 163.8 ms | ≤ 6 | ≤ 0.12 %
USB-Serial-JTAG, 12 Mbit/s line | 21.8 ms | ≤ 45 | ≤ 0.93 %
PARLIO lane, 2 bit × 40 MHz (planned) | 3.3 ms | ≤ 287 | ≤ 5.9 %
PARLIO, 8 bit × 40 MHz (ceiling) | 0.8 ms | ≤ 977 | ≤ 20 %
What this means
Raw snapshots suit calibration research, beamforming and offline algorithm work — the first milestones.
Doppler and tracking need many snapshots with no retune in between (a C5 retune takes ~28–35 ms at 5 GHz).
The planned 2-bit PARLIO lane drains a full snapshot in 3.3 ms — about 7× faster than USB at its line rate.
Notes: What ESP-SDR offers on the C5 today: snapshots of at most 16,380 samples, sent slowly over USB. This is the starting point of step 1.

## Slide 13: Five ways to collect the data
Effort and suitability are judgements for a student team. E is the current team proposal.
13
 | A · Direct to host | B · Ethernet per C5 | C · Central FPGA | D · 4 × 2×2 FPGA tiles | E · 2 × 8 tiles, PARLIO → S31
Topology | each C5 → USB hub → PC | C5 → W5500 → switch → GbE | 16 C5 → one FPGA → Ethernet | 4 × (4 C5 → FPGA) → hub | 8 × 2-bit PARLIO → S31 → RTL8211F → GbE
Good for | bring-up, 1–4 channels | separate networked nodes | deterministic capture, DSP | local reduction, scaling | cheap integrated tile, two uplinks
Data limit | USB full speed per C5 | SPI bridge ≤ 100 Mbit per C5 | 16 C5 slave ports | ¼ of the array per tile | 80 Mbit/s per lane, 640 per tile
Sample alignment | software only | none from Ethernet | ns, in fabric | ns inside a tile | shared PCLK + GO; to be proven
Hardware effort | low | high: 8 bridges + PHYs + switch | high: dense board | high: FPGA per tile | medium: one S31 + one PHY per tile
Where it fits | step 1 | rejected | Plan B variant | Plan B variant | Rev 1 baseline
Notes: Five ways to collect the data. E is the team proposal: no Ethernet per element, one S31 and one PHY per tile. C and D are the FPGA variants we keep as Plan B.

## Slide 14: Two 8-element tiles and one timing board
Team architecture of 13 Oct 2026. Part numbers are candidates. PARLIO export from the C5 and lockstep alignment of eight lanes are open bench questions.
14
Master timing / RF board
48 MHz TCXO
+ fan-out → 16 C5
40 MHz data clock
+ fan-out → PARLIO
Trigger / GO
common capture start
5.2 GHz source
MAX2871-class + 1:2
Tile A — 8 × ESP32-C5 (2 × 4)
C5
C5
C5
C5
C5
C5
C5
C5
ESP32-S31
16-bit PARLIO in
8 × 2-bit @ 40 MHz
PHY
RTL8211F
RGMII
1 GbE
Tile B — 8 × ESP32-C5 (2 × 4)
C5
C5
C5
C5
C5
C5
C5
C5
ESP32-S31
16-bit PARLIO in
8 × 2-bit @ 40 MHz
PHY
RTL8211F
RGMII
1 GbE
Host PC
2 × GbE NIC
bit de-interleaving
calibration, FFT
beamforming, AoA
radar / sensing
48 MHz RF reference
40 MHz PARLIO clock
trigger
5.2 GHz calibration
data
Notes: A master timing / RF board provides the 48 MHz reference, the 40 MHz PARLIO clock, the trigger and the 5.2 GHz calibration tone. Two identical tiles each send one Gigabit stream to the host.

## Slide 15: One tile: eight C5s, one S31, one Gigabit port
C5 PARLIO: datasheet v1.5. S31 EMAC 10/100/1000 over MII/RMII/RGMII with IEEE 1588 (datasheet v0.5). Espressif's S31 board and ESP-SDR use a YT8531 RGMII PHY.
15
Patch
5.2 GHz
SPDT
ANT / CAL
ESP32-C5
IQ snapshot → PARLIO TX
×8
ESP32-S31
16-bit PARLIO RX, external PCLK
GDMA into RAM
sync-word check per frame
UDP packetization
EMAC → RGMII
READY / GO, ANT / CAL GPIOs
IEEE 1588 timestamps
USB HS for debug
2 bit × 40 MHz
READY / GO
PHY
RTL8211F
10/100/1000
RGMII
MagJack
RJ45
1 GbE
1:8 splitter
1:8 buffer 48 MHz
XTAL_P
1:10 buffer 40 MHz
PCLK
ANT / CAL via C5
from master: 5.2 GHz
from master: 48 MHz
from master: 40 MHz
Chip-down C5 (QFN48): modules carry their own 48 MHz crystal and cannot share a reference.
PHY: RTL8211F is the team's choice; Espressif's S31 board uses a YT8531 — check the ESP-IDF driver before layout.
The S31 forwards 16-bit words untouched; bit de-interleaving runs on the host.
Ethernet and PTP give timestamps and coordination only — sample alignment comes from the shared PCLK, the GO signal and the RF calibration.
8 × 80 Mbit/s = 640 Mbit/s on one 16-bit bus at 40 MHz — 64 % of a Gigabit link. No Ethernet MAC, PHY, magnetics or switch per element.
Notes: One lane drawn, eight per tile. C5s are chip-down so XTAL_P can take the shared reference. The S31 receives 16 bits at 40 MHz and forwards them over RGMII to a Gigabit PHY.

## Slide 16: Eight 2-bit streams on one 16-bit bus
C5 TRM v1.1 §43: PARLIO ≤ 40 MHz, external TX clock, not an ETM peripheral; a gated external clock may start after TX_START. Lockstep across chips is an inference to test.
16
40 MHz PCLK
C5 #0
D[1:0]
C5 #1
D[3:2]
C5 #2
D[5:4]
C5 #3
D[7:6]
C5 #4
D[9:8]
C5 #5
D[11:10]
C5 #6
D[13:12]
C5 #7
D[15:14]
ESP32-S31
PARLIO RX
16 bit × 40 MHz
same PCLK at the receiver
Start sequence
1 the S31 arms all C5s; each captures a snapshot and loads its PARLIO DMA descriptors
2 each C5 raises READY
3 the S31 waits until all eight READY lines are high
4 GO: the S31 enables the PCLK buffer, so all lanes start on one edge
5 all C5s shift out on the same clock edges
6 the S31 captures 16-bit words by DMA
7 every frame starts with a sync word common to all lanes
Per-lane frame (every C5 sends the same layout)
Field | bits | Purpose
sync word | 32 | identical on all lanes → alignment check
channel ID | 8 | which C5 / antenna
frame sequence | 16 | detects lost frames
sample counter | 32 | ties the frame to the capture start
capture metadata | 32 | rate, gain index, ANT / CAL state
payload | N × 16 | IQ8 (or packed IQ10)
CRC | 16 | bit errors on the parallel bus
If one lane slips by a clock, the sync word no longer lines up across the 16 bits and the S31 sees it at once. Bit transposition is cheap on a PC and expensive on the S31 at 40 M words/s.
Notes: Each C5 owns two bits of the S31's 16-bit bus. All lanes must stay cycle-aligned, so they share one PCLK and start together after a READY / GO handshake. A common sync word at the start of each frame makes misalignment visible immediately. Bit de-interleaving is left to the PC.

## Slide 17: Two data modes
ESP-SDR C5 limits: rates 80/40/20/10/8/4 MS/s, ≤ 16,380 samples per snapshot, 11–48 MHz analog bandwidth. Lane = 2 bit × 40 MHz = 80 Mbit/s.
17
Mode 1 — continuous reduced rate
Every C5 streams a narrow band continuously over its own 2-bit lane.
Sample rate (nearest ESP-SDR rate) | 4 MS/s, IQ8
Per element | 64 of 80 Mbit/s
Per tile / array | 512 Mbit/s / 1.02 Gbit/s
Instantaneous bandwidth | ≈ 4 MHz
Doppler at 5.2 GHz | 34.7 Hz per m/s
5 MS/s is not an ESP-SDR rate, and 8 MS/s (128 Mbit/s) does not fit a 2-bit lane.
The C5 has no continuous capture today. Back-to-back 4 MS/s snapshots (4.1 ms each, 3.3 ms to drain) would be near-continuous if capture and transfer can overlap.
The C5 analog filter is at least 11 MHz wide: at 4 MS/s out-of-band signals may alias (the S31 stream subsamples without a decimation filter).
On the S31, ESP-SDR streams by routing the modem debug bus into PARLIO. The C5 lists MODEM_DIAG0–31 signals, but IQ on them is undocumented — and 16–20 lanes per C5 would not fit the shared bus.
Mode 2 — full-rate synchronized snapshots
All 16 elements capture the same 205 µs at 80 MS/s, then drain over their lanes.
Snapshot | 16,380 samples, 205 µs
Size per element, IQ8 / IQ10 | 32.8 / 41.0 kB
Drain time at 80 Mbit/s | 3.3 / 4.1 ms
Max snapshot rate (IQ8) | ≈ 287 per second
Array data per snapshot | 524 kB
Wide instantaneous bandwidth (11–48 MHz analog) with low-cost networking.
Right mode for calibration, wideband channel sounding and radar trials.
Needs PARLIO export firmware and a hardware capture trigger — both new work.
Confirmed
Engineering inference
Open — needs bench test
Notes: Mode 1 needs continuous capture on the C5, which does not exist today — back-to-back snapshots at 4 MS/s may approximate it. Mode 2 uses the full 80 MS/s for 205 µs and drains in about 3.3 ms; it is the realistic first target.

## Slide 18: Data-rate budget, stage by stage
Assumptions: IQ8, 16,380-sample snapshots (ESP-SDR maximum on C5), 2 bit × 40 MHz per lane. Replace with step-1/2 measurements.
18
Stage | per element | per tile (×8) | array (×16) | comment
Internal IQ, 80 MS/s, IQ8 | 1.28 Gbit/s | 10.2 Gbit/s | 20.5 Gbit/s | inside the chip only
Snapshot, 16,380 samples (IQ8) | 32 KiB | 256 KiB | 512 KiB | 205 µs of signal
Today: USB-Serial-JTAG | 12 Mbit/s | — | — | ESP-SDR, line rate
PARLIO lane, 2 bit × 40 MHz | 80 Mbit/s | 640 Mbit/s | 1.28 Gbit/s | 64 % of GbE per tile
Mode 1: 4 MS/s IQ8 continuous | 64 Mbit/s | 512 Mbit/s | 1.02 Gbit/s | C5 continuous capture is open
Mode 2: snapshot drain (IQ8) | 3.3 ms | same, parallel | same, parallel | ≤ 287 snapshots/s
64 FFT bins per snapshot, 100/s | 205 kbit/s | 1.64 Mbit/s | 3.28 Mbit/s | complex, 16-bit I/Q
16 × 16 covariance, 100/s | — | — | 870 kbit/s | 136 complex float32
Per tile the lanes add up to 640 Mbit/s and one Gigabit port; the array needs two ports at the host. Reduction (FFT bins, covariance) can move to the S31 or an FPGA later.
Notes: Per tile the lanes add up to 640 Mbit/s, one Gigabit port; two ports at the host. Reduction products are orders of magnitude smaller and can move to the S31 or an FPGA later.

## Slide 19: What happens to the IQ data?
Lane = 2 bit × 40 MHz. S31 PARLIO→GbE at 640 Mbit/s is shown by ESP-SDR's S31 streaming firmware (one board, internal source).
19
ESP32-C5 ×16
ESP32-S31 ×2
Host capture 2 × GbE
Host DSP
80 Mbit/s per lane
(2 bit × 40 MHz)
640 Mbit/s per tile
on 1 GbE
≈ 1.3 Gbit/s total
into RAM
capture on common trigger
snapshot or 4 MS/s stream
frame: sync, ID, counters
PARLIO TX on shared PCLK
16-bit PARLIO RX by DMA
sync-word alignment check
UDP packets, timestamps
ANT / CAL and READY / GO
two NIC ports
bit de-interleaving
frame / sequence checks
dataset recording
(φₖ, τₖ) calibration per FFT bin
beamforming, AoA / MUSIC
radar and sensing
later: move to S31 / FPGA / GPU
The bottleneck is still inside each C5 — capture memory and how fast the IQ reaches PARLIO. Everything after the S31 is ordinary Gigabit networking; the host does the heavy DSP at first.
Notes: Everything after the S31 is ordinary networking. Early on, the PC does all DSP: unpacking, calibration, FFT, beamforming, AoA, radar.

## Slide 20: Plan B: a small FPGA between the C5s and the S31
Candidate FPGAs: Lattice ECP5 / iCE40 UltraPlus (open toolchain), Efinix Trion. Optional for Rev 1.
20
C5 #0
C5 #1
C5 #2
C5 #3
⋮ (×8)
own clock each
small FPGA
8 independent PARLIO receivers
elastic FIFO per channel
frame alignment, timestamps
trigger and switch sequencing
calibration correction
decimation / FFT
later: beamforming
ESP32-S31
or GbE PHY
1 GbE
Switch to Plan B if
eight C5 lanes cannot be kept in lockstep
the S31 cannot sustain 640 Mbit/s in and out
real-time per-element processing (FFT, decimation) is needed
What it costs
one more chip, toolchain and HDL work
more power and board area
the team needs FPGA experience
What it adds
each C5 can run on its own lane clock
deterministic, inspectable timing
data reduction before Ethernet
a path to real-time beamforming
Notes: If eight C5 lanes cannot be kept in lockstep, or the S31 cannot sustain 640 Mbit/s in and out, a small FPGA takes over the per-lane capture and alignment.

## Slide 21: Tile PCB: geometry, seam and stack-up
To scale for 28.8 mm pitch. Custom 4-layer stack (JLCPCB's standard one has only 0.21 mm under L1). Patch: εr 4.4, tan δ 0.02; lossless BW ≈ 3.77·(εr−1)/εr²·(W/L)·(h/λ₀); efficiency counts dielectric loss only. Prices: team estimates.
21
Tile A (≈150 × 100 mm)
back: S31, PHY, clock buffers, power
Tile B (≈150 × 100 mm)
back: S31, PHY, clock buffers, power
seam
14.4 mm
To scale: the 2 × 4 antenna block sits against the seam. Front: patches only. Back: each C5 under its own patch, the rest on the outer half. Rows keep 28.8 mm pitch across the seam only if each board edge is 14.4 mm from its nearest row.
Rev 1 stack-up (custom 4-layer FR-4)
L1 | patches only (the front)
L2 | solid ground (patch ground)
L3 | ground; clock lines, 3.3 V spine
L4 | all parts, RF, data lines
Fab cost (team estimate)
standard 4-layer, 5 boards | $25–35
+ ENIG, impedance control | $35–55
Rev 1 custom stack + blind vias | quote
per tile (standard, 5 boards) | $7–11
6-layer, per board | $10–16
shipping to Israel | $20–35
The patch substrate
A standard 1.6 mm 4-layer board has only ≈ 0.21 mm between L1 and L2: a 5.2 GHz patch there radiates at most ≈ 18 % of its power on FR-4 (lossless bandwidth ≈ 0.3 %; the loss makes the S11 dip look wider than it is).
Rev 1 uses a custom stack with a 1.065 mm core under L1: ≈ 1.6 % (≈ 85 MHz) lossless bandwidth and at most ≈ 53 % efficiency; patch ≈ 17.5 × 13.5 mm, trimmed after a test coupon (≈ 55 MHz per 0.1 of εr).
Front: patches only (plus tented through-via pads). Each C5 sits behind its own patch: probe via, 1 mm to the SPDT, 2.5 mm to the C5, the same for all eight. All digital lines run behind the L2 ground.
Seam: the ground is cut between tiles, so bridge it continuously and calibrate per element. Tile B is turned 180°, so elements 9–16 carry a fixed 180° term.
Notes: Two constraints drive the tile layout. First, the antenna block must sit against the seam so rows stay 28.8 mm apart across boards. Second, a patch on the thin 0.21 mm L1–L2 dielectric of a standard 4-layer board radiates poorly, so Rev 1 uses a custom stack with a 1.065 mm core under the patches. The front carries only the patches; each C5 sits behind its own patch, and all digital lines are behind the L2 ground.

## Slide 22: First useful experiment: receive beamforming
Array factor computed for ideal isotropic elements; real embedded patterns and coupling will differ.
22
Chart: angle (degrees)
Array factor of one 4-element row at λ/2, uniform weights. Half-power beamwidth ≈ 25° at broadside, first sidelobe −11.3 dB. The full 4×4 array steers in both azimuth and elevation.
Experiment
Place a 5.2 GHz CW or Wi-Fi source in the far field (2D²/λ ≈ 0.9 m for the 163 mm aperture diagonal; use ≥ 1 m).
Calibrate with the internal tone, then capture snapshots with the source at known angles.
Form beams digitally: y = wᴴx with w = steering vector; scan azimuth and elevation.
Estimate angle with conventional beamforming and MUSIC; add a second source for nulling.
Success criterion
The measured beam pattern matches the predicted one to within a few dB in the main lobe.
The estimated angle repeats after a power cycle and retune — proving that calibration, not luck, produced coherence.
Notes: Receive steering is purely digital: rotate each element's IQ and sum. The real success test is repeatability after a power cycle — that proves the calibration works.

## Slide 23: Radar experiments
Status = evidence on ESP32-class hardware. Literature: Chetty 2012, Colone 2011, Yildirim 2020, Euchner 2025 (passive channel charting). f_D = 2v/λ; Δr = c/2B.
23
 | Experiment | What we would measure | Evidence and dependencies
 | Wi-Fi sensing from CSI | motion, presence, gestures, breathing-scale phase | widely shown on ESP32; C5 CSI gives 52–242 subcarriers
 | Passive radar / localization with AP illuminators | AoA, Doppler, multipath changes, position | ESPARGOS passive localization at 2.4 GHz; needs mode 1 or fast snapshots
 | Separate TX and RX elements | 1–2 C5s transmit packets, 14–15 receive coherently | standard packet TX; ESPARGOS radar mode does one-TX / rest-RX
 | Pulsed / switched (TDM) | transmit a burst, switch to RX, capture echoes | C5 is half-duplex; TX→RX switching time unknown
 | Active CW or stepped frequency | Doppler (CW), coarse range (stepping) | 5 GHz tone from a C5 undocumented
 | FMCW-like on the same radio | range–Doppler maps | needs simultaneous TX + RX and arbitrary TX — not the starting point
Doppler at 5.2 GHz is 34.7 Hz per m/s; 0.5 m/s resolution (walking people) needs ≈ 60 ms of coherent slow time. Mode 1 at 4 MS/s or back-to-back snapshots make this possible; USB-only snapshots do not.
Range resolution is c/2B: 7.5 m at 20 MHz, ≈ 3.1 m at the C5's 48 MHz analog limit. Angle and Doppler are the strengths.
Confirmed
Engineering inference
Open — needs bench test
Speculative
Notes: Realistic radar modes respect that the C5 is half-duplex: passive radar, separate TX and RX elements, and pulsed / switched operation. Continuous FMCW on one radio is not the starting point.

## Slide 24: Communications experiments
Receive-side items need calibrated coherent capture or CSI; the TX item depends on the open questions on the next slide.
24
 | Experiment | Content | Builds on
 | Receive beamforming | steer a digital beam to a Wi-Fi station; measure SNR gain against one element | calibrated snapshots
 | Interference nulling | two transmitters; place a null on one, keep the other | covariance estimation
 | Wi-Fi angle of arrival | AoA of real stations from per-packet CSI — shown at 2.4 GHz by ESPARGOS | CSI mode + calibration
 | MIMO channel measurements | 16-element channel matrices, multipath, angle–delay profiles | CSI or raw snapshots
 | Localization and beam tracking | follow a moving station; compare with ground truth | repeated snapshots / CSI
 | Distributed coherent TX | beam-steered transmission from several C5s | TX phase control (open)
Confirmed
Engineering inference
Open — needs bench test
Speculative
Notes: Communications experiments reuse the receive chain; coherent TX depends on the open TX questions.

## Slide 25: Transmit: what we know and what we don't
C5 datasheet v1.5; ESP-SDR README, issue #3; ESP-IDF esp_phy_cert_test.h; ESPARGOS One manual §9.4; ECC/DEC/(04)08; Israeli regs 2021.
25
 | Capability | Evidence / comment
 | Standard Wi-Fi packet TX at 5 GHz on every C5 | datasheet: 18 dBm typ. at low rates (chip level)
 | One element transmits, the others receive (TDM) | ESPARGOS One radar mode does this at 2.4 GHz
 | All TX carriers on the same frequency | follows from the shared 48 MHz reference
 | Known, repeatable TX LO phase after each PLL lock | unknown; RX calibration does not measure the TX path
 | Simultaneous TX start on 16 chips | packet TX timing belongs to the Wi-Fi MAC, not to us
 | CW tone at 5 GHz on the C5 | cert-test API esp_phy_wifi_tx_tone() is documented for channels 1–14 only
 | Arbitrary IQ playback on the C5 | ESP-SDR is receive-only; its authors say arbitrary TX works but are not releasing it (misuse and certification concerns)
 | 16-element coherent transmit beamforming | needs all of the above plus over-the-air TX calibration
Regulation: 5150–5250 MHz allows 200 mW EIRP, indoor, in both the EU and Israel, for EN 301 893 RLAN equipment. Sixteen coherent elements add up to 24 dB over one, and custom radar waveforms are probably not covered — do TX experiments cabled, shielded or at low power, on channels 36–48.
Confirmed
Engineering inference
Open — needs bench test
Speculative
Notes: Packet TX is standard; phase-controlled TX is not public. ESPARGOS says it achieved coherent TX on ESPARGOS One but has not released it. Regulation (200 mW EIRP indoors) and 24 dB of array gain argue for cabled or shielded TX tests.

## Slide 26: Transmit steering: easy maths, hard hardware
Phase steps for λ/2 spacing. ESPARGOS states phase-coherent TX works on ESPARGOS One but has not released it (ESP-SDR page, issue #3).
26
Phase step between neighbours at λ/2
Δφ = −π · sin θ, sk[n] = s[n] · ejkΔφ
steering angle θ | Δφ per element
0° | 0°
15° | −46.6°
30° | −90.0°
45° | −127.3°
60° | −155.9°
What is actually hard
Phase-coherent TX LOs: a shared 48 MHz fixes frequency, not the phase after each PLL lock.
Deterministic TX start: normal packet TX is timed by the Wi-Fi MAC, not by us.
A raw TX waveform path on the C5 — the ESP-SDR authors say arbitrary TX works but have not released it.
The C5 is 1T1R and half-duplex: one chain switches between TX and RX.
If steering is needed before that is solved
Separate roles: 1–2 C5s transmit, the other 14–15 receive coherently.
TDM / MIMO: one element transmits at a time, the TX aperture is synthesized afterwards (as in ESPARGOS radar mode).
External RF phase shifters after each C5 — more BOM, loss and control lines; not for Rev 1.
Notes: The steering maths is trivial; the hardware is not. Until raw coherent TX exists, use separate TX/RX roles or TDM-MIMO; external phase shifters are possible but not for Rev 1.

## Slide 27: Power, heat and board constraints
C5: datasheet v1.5 Table 5-8 (peak, 3.3 V). S31, PHY and master-board figures are planning estimates — measure in steps 2 and 4.
27
Supply estimate (3.3 V rail)
Load | per unit | count | total
ESP32-C5, receive (5 GHz) | 110 mA | 16 | 1.76 A
ESP32-C5, transmit peak (5 GHz) | 408 mA | 16 | 6.53 A
ESP32-S31 + RTL8211F (estimate) | ≈ 400 mA | 2 | 0.80 A
Clock buffers, oscillators, SPDTs | ≈ 40 mA | 6 | 0.24 A
Master board incl. synthesizer | ≈ 200 mA | 1 | 0.20 A
All receiving |  |  | 3.0 A · 10 W
All transmitting (worst case) |  |  | 7.8 A · 26 W
Espressif asks for ≥ 0.6 A of supply capability per C5: 4.8 A per tile. Plus 10 µF on each VDDA rail.
TX bursts droop a shared rail and can disturb the reference — give clock buffers and oscillators their own quiet LDO.
Heat: ≈ 10 W in receive over two tiles is easy; continuous all-TX (26 W) needs airflow.
Board-level points
Two tile PCBs, custom 4-layer FR-4 with controlled impedance; one master timing / RF board.
Front: patches only. Each chip-down ESP32-C5 sits behind its own patch, so XTAL_P can take the shared 48 MHz.
PARLIO lines on L4, series-terminated; ≈ 1.2 ns of layout skew (data plus PCLK) and the C5 clock-to-out spread (a bench test) against the 12.5 ns half-period.
48 and 40 MHz point-to-point from 1:8 / 1:10 buffers: on L3 from the buffers, the last few cm to each C5 on L4; series-terminated, away from RF lines.
RF: 50 Ω lines on L4 over a solid L3 ground; each SPDT 1 mm from its probe via and 2.5 mm from its C5.
Antenna substrate: the 1.065 mm core under L1 (see the tile PCB slide).
Notes: Receive-only operation is about 10 W for the whole system. All-TX bursts need roughly 8 A at 3.3 V; Espressif asks for 0.6 A of supply capability per C5.

## Slide 28: What a tile and the full array cost
Team low-volume estimates (Oct 2026), not quotes. Excludes lab instruments, enclosure and engineering time.
28
One 8-element tile (electronics)
Item | ≈ USD
8 × ESP32-C5 (chip-down needed for a shared reference) | 40
1 × ESP32-S31 | 7.5
1 × RTL8211F Gigabit PHY | 1.4
Gigabit MagJack | 2.5
48 / 40 MHz fan-out buffers | 7.5
40 MHz oscillator | 1.5
8 × RF SPDT (SKY13351-class) | 5
3.3 V regulation, power | 3
Ethernet crystal, passives, misc. | 3–5
Tile electronics | 70–80
Full 16-element system
Item | ≈ USD
Two tiles | 140–160
Master board: 48 MHz, trigger, 5.2 GHz source, splitters | 15–20
Electronics total | 160–180
PCBs, assembly, shipping | 60–120
Complete prototype target | 220–300
Chip-down C5s replace modules because modules carry their own crystal; parts cost is similar, layout work is higher.
The custom stack-up (with blind L4–L3 vias) keeps the patches on the tile but needs a quote: the PCB line assumes standard-stack prices. Ask for a balanced build and a bow/twist limit. A separate antenna board would add a second fab order and 16 RF connections.
A MAX2871 evaluation board alone costs more than the $15–20 line; a bare synthesizer on the master board is assumed.
For scale: an ESPARGOS One Core Kit (8 elements, 2.4 GHz, finished product with enclosure, PoE and firmware) is €350 excl. VAT.
Notes: Team estimates, not quotes: about $70–80 of electronics per tile and $220–300 for a complete prototype. Chip-down C5s replace modules because modules carry their own crystal.

## Slide 29: Software stack
Everything above the C5 firmware is ordinary open tooling; the C5 layer depends on ESP-SDR and ESP-IDF internals.
29
ESP32-C5 firmware
ESP-SDR capture (pinned IDF)
fixed gain, RF tuning
trigger input, READY
pack IQ8 / IQ10
PARLIO TX by GDMA
frame header: sync, ID, counters
ESP32-S31 firmware
16-bit PARLIO RX by DMA
lane alignment check
READY / GO, ANT / CAL
UDP packetization
PTP timestamps
control API
Host
two GbE capture threads
bit de-interleaving (NumPy)
frame / sequence checks
calibration (φₖ, τₖ per bin)
beamforming, MUSIC, radar
Python, SciPy; MATLAB optional
Later
reduction on the S31
FPGA preprocessing (Plan B)
GPU (CuPy) for real-time
GNU Radio blocks
dataset publishing
Visualization
beam pattern
AoA / MUSIC spectrum
spectrogram
range–Doppler map
per-element phase vs time
calibration health
Every captured snapshot is stored with its calibration state, so results can be re-processed offline.
Notes: C5 firmware builds on ESP-SDR (pinned toolchain) plus a PARLIO exporter. The S31 firmware is a DMA-to-UDP pipe with alignment checks; the host does the science.

## Slide 30: Critical bench experiments before the tile PCB
Status = what is already stated or shown in a primary source, not on our hardware. Evidence: ESP-SDR source and docs, ESP32-C5 / S31 datasheets, ESPARGOS papers.
30
 | Test | What it proves | Evidence today
 | C5 raw IQ → GDMA → PARLIO TX | a snapshot can leave the C5 without CPU copies | GDMA can address the ESP-SDR IQ bank; ESP-SDR packs IQ8 in place on the CPU; access while the modem owns the bank is unknown
 | 2 bit × 40 MHz from one C5 | 80 Mbit/s per element in practice | 40 MHz is PARLIO's maximum clock; receiver samples on the falling edge (≈ 12.5 ns window)
 | eight C5 PARLIO transmitters in lockstep | Rev 1 needs no FPGA | PARLIO has no ETM start; the reference manual's gated external clock suggests a clock-held start — untested
 | 16-bit PARLIO RX at 40 MHz into the S31 | tile ingress | ESP-SDR S31: 16-lane PARLIO → GDMA ring at 40 MS/s, but fed internally with an internal sample clock — external pins + PCLK untested
 | S31 → GbE at ≈ 640 Mbit/s | tile egress | ESP-SDR: raw UDP frames at ≈ 687 Mbit/s, 600 s, 0 samples lost (one board, experimental)
 | shared 48 MHz into C5 XTAL_P | frequency lock across elements | no C5 guidance; ESP32-S2 oscillator note, ESPARGOS at 40 MHz
 | RF phase repeatability: reset, retune, temperature | how often to calibrate | ESPARGOS: phase re-rolls at 2.4 GHz; C5 unmeasured
 | snapshot synchronization on a wideband signal | real phase, delay and jitter | ESPARGOS One: ≤ 37.5 ns timestamp scatter (2.4 GHz, closed firmware)
Confirmed
Engineering inference
Open — needs bench test
Notes: Eight bench experiments decide the PCB. Two are partly de-risked already: ESP-SDR shows 16-lane PARLIO capture and ≈ 687 Mbit/s Gigabit streaming on one S31. The C5-side tests are all open.

## Slide 31: Development sequence
Each step ends with a measurable result; nothing larger is built until the previous step passes.
31
1 One C5
run ESP-SDR
characterise raw IQ
inspect memory / DMA path
implement PARLIO export
Done when
a snapshot leaves over PARLIO, bit-exact
2 C5 + S31
2-bit PARLIO, shared 40 MHz
≈ 80 Mbit/s stream
out over GbE
Done when
80 Mbit/s to the PC for hours, no loss
3 Two C5s
common 48 MHz reference
common trigger
phase calibration
first AoA
Done when
relative phase stable to a few degrees
4 Eight C5s
full tile
16-bit PARLIO, ≈ 640 Mbit/s
receive beamforming
Done when
8 lanes aligned for hours; beam matches prediction
5 Second tile
16 elements
common calibration
4 × 4 AoA and beamforming
Done when
calibrated 2D scan, repeatable after power cycle
6 Extensions
radar, Wi-Fi sensing
coherent TX research
digital TX beamforming
FPGA preprocessing
Done when
research results
Notes: Six steps, each ending with a measurable result. Nothing larger is built until the previous step passes; step 3 (two C5s on one reference) is the key go / no-go point.

## Slide 32: Main technical risks
The first eight are the team's list; the last two came out of the research. Each except coherent TX (step 6) has a bench test in steps 1–4.
32
Risk | Early test | Fallback
C5 raw IQ cannot reach PARLIO by DMA at the needed rate | step 1: snapshot → PARLIO, bit-exact | CPU copy at lower rate; snapshots only
Eight lanes not cycle-aligned (40 MHz is PARLIO's limit) | steps 2 and 4: sync-word checks, eye margin | Plan B: FPGA with per-lane FIFOs
S31 cannot ingest and send 640 Mbit/s at once | step 2 → 4: 80 → 640 Mbit/s | lower lane rate, or FPGA → GbE PHY
Shared 48 MHz gives poor phase stability | step 3: phase vs time and temperature | per-snapshot calibration
C5 LO phase not repeatable across resets / retunes | step 3: repeated resets and retunes | calibrate every epoch (as ESPARGOS)
Coherent TX method not reproducible on C5 | step 6, research only | RX-only results stand alone
FR-4 antenna / array consistency insufficient | VNA on the first tile | separate aperture board (ours) or better laminate
Power and heat with 16 active C5s | current and temperature on one tile | duty-cycle TX, airflow
No continuous capture on the C5 (mode 1) | step 1: back-to-back snapshot timing | mode 2 only; quasi-continuous snapshots
Custom stack: cost, warpage; patches lossy (≤ 53 %) | quote; simulate + VNA one tile | standard stack + our aperture board
Notes: The team's eight risks plus two from the research: no continuous capture on the C5, and patches that stay narrowband and lossy on FR-4.

## Slide 33: What we know, what we infer, what we must test
Checked 12–13 Oct 2026 against the references; open items become bench tests in phases 1–2.
33
 | Claim | Basis
 | ESP32-C5 receives 5180–5885 MHz; 1T1R; 18 dBm TX, −94 dBm sensitivity (low rates) | Espressif datasheet v1.5
 | ESP-SDR raw IQ on C5: 80/40/20/10/8/4 MS/s, ≤ 16,380 samples, USB / UART out | ESP-SDR source and README
 | C5 PARLIO TX: 1/2/4/8 bit, ≤ 40 MHz, external clock pad, GDMA; not an ETM peripheral | C5 TRM v1.1, ESP-IDF source
 | S31 streams 16-lane PARLIO capture to GbE at ≈ 687 Mbit/s (experimental) | ESP-SDR S31 docs; 600 s, 0 lost
 | S31 EMAC: 10/100/1000, MII / RMII / RGMII, IEEE 1588 timestamps | S31 datasheet v0.5 (pre-release)
 | ESP32-C5 modules integrate their own 48 MHz crystal | module datasheet v1.3
 | ESP32 PLL phase changes after reset and retune | ESPARGOS hardware paper
 | 2-bit lanes from eight C5s can be packed into one 16-bit S31 bus | PARLIO widths and clocks
 | A 2-bit lane carries 4 MS/s IQ8 continuously (64 of 80 Mbit/s) | arithmetic
 | C5 IQ buffer → GDMA → PARLIO without CPU copies | untested
 | Eight C5 PARLIO transmitters stay in lockstep | untested
 | XTAL_P can be driven cleanly from a shared 48 MHz buffer | not documented for C5
 | Continuous IQ capture on the C5 | no C5 continuous mode today
 | Coherent TX on C5 | ESPARGOS: works on ESPARGOS One, unpublished
 | 16-element coherent TX beamforming | no evidence yet
Confirmed
Engineering inference
Open — needs bench test
Speculative
Notes: The evidence summary. Notice how much of the C5 side is still open — that is the research content of the project.

## Slide 34: Alternatives we considered
Design-decision record. BCM53202M product brief (Broadcom 53202M-PB00-R): 8 × 10/100 PHYs, two GMII/RGMII/TBI ports, 384 KB buffer.
34
Alternative | Why not for Rev 1 | Reconsider when
W5500 SPI-Ethernet per C5 | C5 has no MAC; adds 8 bridges, PHYs, magnetics and a switch; 100 Mbit ceiling per element | single-node experiments, elements on separate boards
Ethernet switch per tile (BCM53202M: 8 × 10/100 + 2 × GbE) | needs Ethernet on every C5 first; solves aggregation, not sample synchronization | elements become separate networked boards
ESP32-S31 as the RF element (2.4 GHz) | continuous IQ works today, but 2.4 GHz only: new aperture, crowded band | if C5 PARLIO export fails
4 × 2×2 tiles, one FPGA each | more boards, FPGA mandatory, four uplinks | Plan B, or more processing per tile
Analog phase shifter per element | receive steering is exact and wideband in software | deterministic TX steering before raw TX exists
Buy 2 × ESPARGOS One (2.4 GHz) | closed IQ firmware, 2.4 GHz, not our design | as a reference instrument and baseline
Notes: Design-decision record: why not Ethernet per element, why not a switch, why not 2.4 GHz S31 elements, and when we would revisit each.

## Slide 35: What a successful student project looks like
Each tier is a complete project outcome on its own.
35
Minimum
a solid result even if the tile PCB is late
C5 raw IQ exported over PARLIO, measured
C5 + S31 streaming to a PC over GbE
two C5s on one reference, phase-calibrated
open-source code + measurement report
Target
the proposal as planned
one 8-element tile at 640 Mbit/s
two tiles: calibrated 4 × 4 beamforming and AoA
both data modes working
a published dataset of synchronized captures
Stretch
only after the target is met
Doppler / passive radar demo
separate-TX bistatic experiments
first coherent-TX experiments
FPGA or S31 preprocessing
A good outcome is measured coherence and a reusable platform — not a single beam plot. Every result should survive a power cycle.
Notes: Three tiers, each a complete outcome. The minimum tier — C5 IQ over PARLIO, C5 + S31 streaming and two coherent C5s — is already publishable.

## Slide 36: References
36
[1] F. Euchner, T. Schneider, M. Gauger, S. ten Brink, “ESPARGOS: An ultra low-cost, realtime-capable multi-antenna WiFi channel sounder,” WSA & SCC 2023. arxiv.org/abs/2502.09405
[2] F. Euchner, S. ten Brink, “ESPARGOS: Phase-coherent WiFi CSI datasets for wireless sensing research,” 2024. arxiv.org/abs/2408.16377
[3] F. Euchner, D. Kellner, P. Stephan, S. ten Brink, “Passive channel charting: Locating passive targets using Wi-Fi CSI,” 2025. arxiv.org/abs/2504.09924
[4] ESPARGOS One datasheet and Quick Start Manual Rev 1.0, June 2026. espargos.net/espargos-one/
[5] ESPARGOS documentation: phase-coherent multi-array systems; IQ sampling. espargos.net/docs/combined-arrays.html
[6] pyespargos library (LGPL-3.0): iq_sync, iq_pool, iq_tone, csi_calibration. github.com/ESPARGOS/pyespargos
[7] ESP-SDR: raw IQ capture with Espressif’s ESP32 chips (project page). espargos.net/espsdr/
[8] ESPARGOS/esp-sdr (GPL-3.0), HEAD e74f2a4, 8 Oct 2026: README, targets/esp32c5/chip.h, docs/rx-controls.md, issues #3 #5, PRs #6 #9. github.com/ESPARGOS/esp-sdr
[9] Espressif, ESP32-C5 Series Datasheet v1.5, Sept 2026. espressif.com/sites/default/files/documentation/esp32-c5_datasheet_en.pdf
[10] Espressif, ESP32-C5 Hardware Design Guidelines: schematic checklist, PCB layout. docs.espressif.com/projects/esp-hardware-design-guidelines/en/latest/esp32c5/
[11] Espressif, ESP32-C5-WROOM-1/1U Datasheet v1.3; ESP32-S31 Datasheet v0.5 (pre-release). espressif.com/en/support/documents/technical-documents
[12] Espressif, ESP32-S2 Hardware Design Guidelines — oscillator input on XTAL_P. docs.espressif.com/projects/esp-hardware-design-guidelines/en/latest/esp32s2/
[13] Espressif, ESP-Hosted-MCU performance (C5 SDIO throughput). github.com/espressif/esp-hosted-mcu/blob/main/docs/design/performance.md
[14] Espressif, ESP32-C5 Technical Reference Manual v1.1 — Parallel IO (ch. 43), GDMA, ETM. documentation.espressif.com/esp32-c5_technical_reference_manual_en.pdf
[15] Espressif, ESP32-S31 Series Datasheet v0.5 (pre-release), 2026 — PARLIO, Gigabit EMAC with IEEE 1588. documentation.espressif.com/esp32-s31_datasheet_en.html
[16] ESP-SDR, ESP32-S31 streaming notes and test reports (16-lane PARLIO, ESR2 over GbE). github.com/ESPARGOS/esp-sdr/blob/main/docs/s31-streaming.md
Notes: Primary sources: ESPARGOS papers and docs, ESP-SDR source, Espressif datasheets and guidelines.

## Slide 37: References (continued)
37
[17] Espressif, ESP-IDF Parallel IO (PARLIO) TX driver, ESP32-C5. docs.espressif.com/projects/esp-idf/en/latest/esp32c5/api-reference/peripherals/parlio/parlio_tx.html
[18] Analog Devices, MAX2871 23.5–6000 MHz synthesizer with integrated VCO, datasheet. analog.com/en/products/max2871.html
[19] Skyworks, SKY13351-378LF 0.02–6 GHz SPDT switch, datasheet. skyworksinc.com
[20] Broadcom, BCM53202M product brief (53202M-PB00-R). docs.broadcom.com/doc/53202M-PB00-R
[21] Realtek, RTL8211F(I)-CG integrated 10/100/1000 Ethernet transceiver, datasheet. realtek.com
[22] Espressif, esp-csi and the esp-crab two-ESP32-C5 example. github.com/espressif/esp-csi/tree/master/examples/esp-crab
[23] Espressif, ESP-IDF: ESP32-C5 Wi-Fi CSI; esp_phy_cert_test.h (TX tone API). docs.espressif.com/projects/esp-idf/en/latest/esp32c5/
[24] C. Barrett (ed.), “Fractional/Integer-N PLL basics,” Texas Instruments SWRA029, 1999. ti.com/lit/an/swra029/swra029.pdf
[25] Datasheets: TI LMK1C1104 (SNAS791D), Epson TG2016SMN, SiTime SiT5356. ti.com/lit/ds/symlink/lmk1c1104.pdf
[26] K. Chetty, G. E. Smith, K. Woodbridge, “Through-the-wall sensing of personnel using passive bistatic WiFi radar at standoff distances,” IEEE TGRS 50(4), 2012. doi.org/10.1109/TGRS.2011.2164411
[27] F. Colone, K. Woodbridge, H. Guo, D. Mason, C. J. Baker, “Ambiguity function analysis of wireless LAN transmissions for passive radar,” IEEE TAES 47(1), 2011. doi.org/10.1109/TAES.2011.5705673
[28] H. C. Yildirim et al., “High resolution 802.11ax-based passive radar for human movement monitoring,” EuRAD 2020 (held January 2021). research.dial.uclouvain.be/handle/2078.5/218703
[29] S. M. Hernandez, E. Bulut, “Lightweight and standalone IoT based WiFi sensing for active repositioning and mobility,” WoWMoM 2020 (ESP32 CSI Tool). github.com/StevenMHernandez/ESP32-CSI-Tool
[30] CEPT ECC/DEC/(04)08 (amended 2021); Israel Wireless Telegraphy (Conformity Approvals) Regulations 2021. docdb.cept.org/download/3450
[31] h0m3us3r, eSpDR — ESP32-S3 + FPGA raw IQ at 80 MS/s. github.com/h0m3us3r/eSpDR
Notes: Further sources: clocking, radar literature and regulation.